# ZPU - Zylin Soft CPU
Prototype architecture

Whitepaper

V1.6

April 15. 2008
Copyright  2005, Zylin AS
oyvind.harboe@zylin.com

Abstract

This white paper describes the the architecture of the ZPU.

The ZPU is the worlds smallest CPU with a GCC toolchain. It is intended for implementation on FPGAs.

# Stack
The ZPU is a stack based architecture. The stack behaves as most stacks do on modern CPUs.

- The SP register points to the value on top of the stack.
- Pushes predecrement the stack pointer, then store the value on top of the stack
- Pops are postincrement

# Registers
Register name	Description
PC	Contains enough bits to address entire RAM and IO mapped memory.
SP	Contains enough bits to address entire RAM. Bit 0 and 1 are always 0.
IDIM	Flag that determines the behaviour of the IM instructions. Interrupts are masked while the IMM register is set. 1 bit wide.

# Instruction set
Only the base instructions are implemented in the architecture. More advanced instructions, like ASHIFTLEFT are emulated in the illegal instruction vector.

All operations are 32 bit wide.

Name	Opcode	Action
BREAKPOINT	00000000	The debugger sets a memory location to this value to set a breakpoint. Once a JTAG-like debugger interface is added, it will be convenient to be able to distinguish between a breakpoint and an illegal(possibly emulated) instruction.
IM	1xxx xxxx	Pushes 7 bit sign extended integer and sets the a «instruction decode interrupt mask» flag(IDIM). / If the IDIM flag is already set, this instruction shifts the value on the stack left by 7 bits and stores the 7 bit immediate value into the lower 7 bits. / Unless an instruction is listed as treating the IDIM flag specially, it should be assumed to clear the IDIM flag. / To push a 14 bit integer onto the stack, use two consequtive IM instructions. / If multiple immediate integers are to be pushed onto the stack, they must be interleaved with another instruction, typically NOP.
STORESP	010x xxxx	Pop value off stack and store it in the SP+xxxxx*4 memory location, where xxxxx is a positive integer.
LOADSP	011x xxxx	Push value of memory location SP+xxxxx*4, where xxxxx is a positive integer, onto stack.
ADDSP	0001 xxxx	Add value of memory location SP+xxxx*4 to value on top of stack.
EMULATE	001x xxxx	Push PC to stack and set PC to 0x0+xxxxx*32. This is used to emulate opcodes. See zpupgk.vhd for list of emulate opcode values used. zpu_core.vhd contains reference implementations of these instructions rather than letting the ZPU execute the EMULATE instruction.
PUSHPC	emulated	Pushes program counter onto the stack.
POPPC	0000 0100	Pops address off stack and sets PC
LOAD	0000 1000	Pops address stored on stack and loads the value of that address onto stack. / Bit 0 and 1 of address are always 0.
STORE	0000 1100	Pops address, then value from stack and stores the value into the memory location of the address. / Bit 0 and 1 of address are always 0
PUSHSP	0000 0010	Pushes stack pointer.
POPSP	0000 1101	Used to allocate/deallocate space on stack for variables or when changing threads.
ADD	0000 0101	Pops two values on stack adds them and pushes the result
AND	0000 0110	Pops two values off the stack and does a bitwise-and & pushes the result onto the stack
OR	0000 0111	Pops two integers, does a bitwise or and pushes result
NOT	0000 1001	Bitwise inverse of value on stack
FLIP	0000 1010	Reverses the bit order of the value on the stack, i.e. abc->cba, 100->001, 110->011, etc.
NOP	0000 1011	No operation
See zpupkg.vhd for complete list

# Vectors
Address	Name	Description
0x000	Reset	When the ZPU boots, this is the first instruction to be executed. / The stack pointer is initialised to maximum RAM address
0x020	Interrupt(future)	This is the entry point for interrupts. Not implemented yet, but used by the simulator when running eCos.
0x040-	Emulated instructions	Emulated opcode 34. Note that opcode 32 and opcode 33 are not normally used to emulate instructions as these memory addresses are already used by boot vector, GCC registers and the interrupt vector.

# Memory map
The memory map is defined by the GCC libgloss library. See zpuphiregs.odt document
# How to implement and verify a ZPU implementation
The recommended best practice for implementing a ZPU:

- Choose a set of EMULATE instructions to support
- Write up the new ZPU implementation
- Simulate new ZPU and produce a trace.txt file.
- Use the ZPU simulator & GDB to verify that the trace.txt is correct. GDB will break when trace.txt differs from what the simulator expects