Address	Type	Name	Description
0x080A0000	Write	ZPU enable	Bit [31:1] Not used / Bit [0] Enable ZPU operations / 0 ZPU is held in Idle mode / 1 ZPU running
0x080A000C	Read/ / Write	ZPU UART to ARM7 TX / NOTE! ZPU side	Bit [31:9] Not used / Bit [8] TX buffer ready (valid on ready) / 0 TX buffer not ready (full) / 1 TX buffer ready / Bit [7:0] TX byte (valid on write)
0x080A0010	Read	ZPU UART to ARM7 RX / NOTE! ZPU side	Bit [31:9] Not used / Bit [8] RX buffer data valid / 0 TX buffer not valid / 1 TX buffer valid / Bit [7:0] RX byte (when valid)
0x080A0014	Read/ / Write	Counter(1)	Bit [0] Reset counter (valid for write) / 0 N/A / 1 Reset counter / Bit [1] Sample counter (valid for write) / 0 N/A / 1 Sample counter / Bit [31:0] Counter bit 31:0
0x080A0018	Read	Counter(2)	Bit [31:0] Counter bit 63:32
0x080A0020	Read / Write	Global_Interrupt_mask	Bit [31:1] Not used / Bit [0] Global intr. Mask / 0 Interrupts enabled / 1 Interrupts disabled
0x080A0024	Write	UART_INTERRUPT_ENABLE	Bit [31:1] Not used / Bit [0] UART RX interrupt enable / 0 Interrupt disable / 1 Interrupt enable
0x080A0028	Read / Write	UART_interrupt	Bit [31:1] Not used / Bit [0] UART RX interrupt pending (Read) / 0 No interrupt pending / 1 Interrupt pending / Bit [0] Clear UART interrupt (Write) / 0 N/A / 1 Interrupt cleared
0x080A002C	Write	Timer_Interrupt_enable	Bit [31:1] Not used / Bit [0] Timer interrupt enable / 0 Interrupt disable / 1 Interrupt enable
0x080A0030	Read / / Write	Timer_interrupt	Bit [31:2] Not used / Bit [0] Timer interrupt pending (Read) / 0 No interrupt pending / 1 Interrupt pending / Bit [1] Reset Timer counter (Write) / 0 N/A / 1 Timer counter reset / Bit [0] Clear Timer interrupt (Write) / 0 N/A / 1 Interrupt cleared
0x080A0034	Write	Timer_Period	Bit [31:0] Interrupt period (write) / Number of clock cycles / between timer interrupts / NOTE! The timer will start at Timer_Periode value and count down to zero, and generate an interrupt
.0x080A0038	Read	Timer_Counter	Bit [31:0] Timer counter (read)