ZPU
Zylin soft-CPU
Øyvind Harboe
General Manager
Zylin AS

---
ZPU key features
Targeted at FPGA devices
Smallest configuration <500 LUT, 20 DMIPS
Code size consistently <66% of ARM 32 non-thumb
32 bit programming model
GCC toolchain
eCos HAL, popular opensource embedded OS

---
Demo
Xilinx XC3S400 FPGA
Dhrystone 2.1
eCos hello world application

---
Demo - 2
Dhrystone 2.1
  - -Os
  - -O2
  - -O3

---
Demo - 3
eCos hello world
Multithreading
Interrupts support(current ZPU does not have interrupts)
<20kBytes

---
Building FPGA binary image
Compile C++ application:
  - $ zpu-elf-gcc hello.c -o hello.elf -abel
  - “-abel” tells GCC which instruction set and corresponding runtime libraries to use
Convert to VHDL ROM image
  - $ sh genrom.sh hello
Build FPGA binary image using normal procedure

---
ZPU architecture
0 operand/stack based
like the Transputer, x86 FPU, CLR/Java, etc.)
  - IM 5
  - LOADSP 20
  - ADD
8 bit wide instructions
Scales well for range reasonable to implement in FPGA

---
ZPU opcodes
1xxx xxxx IM
  - Pushes 7 bit signed integer onto stack
010x xxxx LOADSP
  - Pushes value at memory address SP+xxxxx*4 onto stack
011x xxxx STORESP
  - Pops value on stack and stores it at address SP+xxxxx*4

---
ZPU opcodes - 2
001x xxxx EMULATE
  - High-level opcodes without further structure, e.g. BRANCH, CALL, RETURN
000x xxxx
  - Low-level opcodes without further structure, e.g. ADD, NOT.

---
ZPU opcodes - 3
The 0 operand architecture allows flexible and small microcode(no HDL changes necessary) for EMULATE category instructions
Smallest ZPU implements 16 instructions, which is > minimum possible # of instructions

---
ZPU GCC backend
GCC is most known for its support of register architectures with a large number of registers
GCC is also used for stack based architectures(e.g. Transputer, x86 FPU)
E.g. M68HC11 has very few registers
ZPU backend uses standard 0-operand techniques and invents some new tricks

---
ZPU GCC backend - 2
The ZPU backend maps the GCC register concept onto stack slots in the stack frame(this different from pseudo registers)
Allows taking full advantage of LOADSP/STORESP
ZPU backend has various unique stack architecture specific optimizations
  - Dead stack slot elimination(similar to REG_DEAD).

---
ZPU GCC backend - 3
0 operand architecture allows excellent code size characteristics
IM + IDIM flag & linker relaxation
  - IM 1	; push 1 onto stack, sets IDIM flag
  - IM 1	; shifts value on stack 7 bits to the left
  - ; and ors in 7 new bits
  - CALL

---
ZPU GCC runtime libraries
Multilib support
  - ZPU alpha HDL
  - More advanced instruction sets
  - Combinations of optimising for size, speed, etc.
Runtime detection of RAM, MHz and IO base, encoded in HDL

---
ZPU GCC testsuite
GCC comes with comprehensive testsuite
The ZPU toolchain passes the entire GCC toolchain testsuite: check-gcc, check-c++, check-libstdc++-v3
Expect <10 issues at any one time during development
  - Need to upgrade to GCC 3.4.3, GDB 6.3
  - A couple of ZPU backend issues that will become moot

---
ZPU simulator
Multiple variants of the ZPU supported
  - ZPU alpha HDL
  - 16 Mbyte RAM version for GCC testsuite
Instruction level profiling histograms
HDL simulation trace file support(more about which later)

---
eCos ZPU HAL
Multiple variants of the ZPU
  - ZPU alpha HDL
  - Simulated w/16 MByte of RAM. Test TCP/IP loopback.
Interrupts support
Diagnostic serial IO

---
ZPU alpha version HDL
Proof of concept
Verification ISS performance model
Small implementation(<500LUT)
32 Kbytes dual-port FPGA RAM
90 Mhz
UART
Performance counters

---
ZPU alpha version HDL -2

---
ZPU alpha version HDL - 3

---
ZPU alpha version HDL - 4
Simulation trace output to file
The GDB server/simulator supports trace file
GDB debugger breaks on ISS != trace file
Useful for debugging early start-up issues
Verify cycle accuracy of ISS performance model

---
ZPU alpha version HDL - 5
Simulation trace output used for ZPU HDL regression testing
Trace integration w/GDB less useful for real-world applications.
Point of diminishing returns as test bench becomes more complicated, e.g. asynchronous UART events

---
ZPU alpha version HDL - 6
Further development should be done on actual target hardware
Completion of memory subsystem
DDR RAM module to increase range of tests
Interrupts
Increase span of configurable performance envelope from(more instructions/pipelining)
More IO => MAC.

---
Eclipse CDT ZPU plugin
Eclipse CDT is a GUI frontend for GDB
Altera, TI, STmicro, etc. choice for IDE
Zylin published a generic embedded GDB plugin 2004
Will be developed with additional ZPU specific GUI components

---
Minimal hello world
Interactive demonstration. Compile & debug.

---
Minimal hello world - 2
Basic hello world, using newlib
eCos TCP/IP loopback test applications

---
Questions?